## Slide 1
ENTERPRISE NETWORK
24/7
Mission Critical
PESI
Pakistan Emergency
Smart Infrastructure
Enterprise Network Infrastructure Analysis
Prepared by: Abdul Wahid
Project: PESI Network Architecture
December 24, 2025
Network Analysis Report

## Slide 2
NAVIGATION
Network Architecture Overview
01
Head Quarter (HQ)
Core Network Infrastructure
9 VLANs
Dual Core
Area 0
02
Branch 2
Redundant Remote Office
6 VLANs
HSRPv2
Area 1
03
Branch 1
Distributed Offices
6 VLANs
NAT/PAT
Area 3
04
(E-Site)
Emergency Response System
10 VLANs
Load Balance
Area 2
05
Central Distribution System
Network Hub & Security Layer
Dual Firewall
DMZ
VPN
Multi-Area OSPF
5 Sites
4 OSPF Areas
Zero Single Point of Failure

## Slide 3
01
Head Quarter
Network
Enterprise-level core infrastructure with 9 VLANs,
dual redundancy, and comprehensive services
9
Department VLANs
Complete segmentation
2
Core Switches
Active-Standby HSRP
7
Critical Servers
Full service stack

## Slide 4
HEAD QUARTER
HQ: Network Core Architecture
Hierarchical 3-tier design with dual redundancy at every layer
Core Layer Infrastructure
Core-Active (Primary L3 Switch)
Router ID: 1.1.1.1 | HSRP Priority: 110 (Active)
Core-Standby (Backup L3 Switch)
Router ID: 5.5.5.5 | HSRP Priority: 90 (Standby)
LACP Port-Channel 1
• 3x GigabitEthernet links bundled
• Load balancing & redundancy
• 3 Gbps aggregate bandwidth
Edge Routing Layer
HQ-Router (Main Router)
Router ID: 3.3.3.3 | Internet connectivity
Standby-HQ (Backup Router)
Router ID: 4.4.4.4 | Redundant internet
OSPF Configuration
Area 0 (Backbone)
• 4 routers in OSPF domain
• Passive interfaces on host networks
• Point-to-point network types on links
4
OSPF Routers
9
VLAN Networks
Redundancy Features
HSRP: Active-Standby gateway redundancy
LACP: Link aggregation with load balancing
RAPID-PVST: Spanning tree optimization
OSPF: Dynamic routing failover
Topology: Hierarchical 3-Tier (Core → Distribution → Access)
IP Scheme: 50.50.0.0/16

## Slide 5
HEAD QUARTER
HQ: VLAN Segmentation & Services
Department-wise network isolation with comprehensive service infrastructure
VLAN Segmentation Table
VLAN | Department | Network | Gateway
10 | Servers | 50.50.10.0/24 | 50.50.10.1
20 | HR Department | 50.50.20.0/24 | 50.50.20.1
30 | Finance Department | 50.50.30.0/24 | 50.50.30.1
40 | Sales Department | 50.50.40.0/24 | 50.50.40.1
50 | IT Department | 50.50.50.0/24 | 50.50.50.1
60 | Management | 50.50.60.0/24 | 50.50.60.1
70 | Voice (VoIP) | 50.50.70.0/24 | 50.50.70.1
80 | IoT Devices | 50.50.80.0/24 | 50.50.80.1
90 | Wireless/WiFi | 50.50.90.0/24 | 50.50.90.1
Critical Servers (VLAN 10)
📧 EMAIL Server
IP: 50.50.10.12 | Domain: pesi.com
🌐 DNS Server
IP: 50.50.10.11 | A Record: pesi.com
📡 DHCP Server
IP: 50.50.10.10 | 9 DHCP Pools
📁 FTP Server
IP: 50.50.10.14 | Department-wise access
🕒 NTP/SYSLOG
IP: 50.50.10.16 | Centralized sync
🔐 AAA/RADIUS
IP: 50.50.10.18 | Port: 1645
🏠 IoT Server
IP: 50.50.10.17 | Registration server
Network Capacity
9
VLANs
~2,000
Devices
HSRP: Virtual IP as default gateway | Preempt: Enabled | Root Bridge: Core-Active (Priority 24576)

## Slide 6
HEAD QUARTER
HQ: VoIP, IoT & Security Implementation
Integrated communication and automated security systems
VoIP/Telephony System
Voice-Path Router
IP: 50.50.100.2
System: Cisco CME (Call Manager Express)
Capacity: 42 IP Phones max
5
IP Phones
6001-6005
Extensions
Dial-Peer Configuration
External calling configured with proper dial-peers for outbound call routing
Security Implementation
SSH Access Control
• SSH version 2 (secure)
• Access-list: SSH-ADMIN-ACCESS
Authorized SSH Hosts (4)
• 50.50.50.23
• 50.50.50.22
• 50.50.90.126
• 50.50.60.21
AAA Authentication
Local & RADIUS authentication with enable secret and privilege level 15 for admin
IoT Security System
System Components
Camera
Always ON (24/7)
Motion Detector
Trigger based
Siren
Motion activated
Smart Door Locks
Auto lock
Automation Logic
Motion Detected
Siren: ON
All Doors: LOCK
IoT Server
IP: 50.50.10.17 | Function: IoT Registration Server | Username: pesi123
Management: Centralized Syslog (50.50.10.16) | NTP Synchronized | HSRP State Tracking

## Slide 7
02
Branch
Networks
Remote office configurations with
scalable architecture and redundant connectivity
3
Branch Sites
Remote offices
100%
Redundancy
Dual everything
1,200+
User Capacity
Per branch

## Slide 8
BRANCH NETWORKS
Branch 2: Scalable Remote Office
Enterprise-grade remote site with HSRPv2, serial backup, and inter-branch connectivity
Network Infrastructure
Dual L3 Core Switches (HSRPv2)
Core-Main-L3
RID: 10.20.255.3
Priority: 110 (Active)
Core-Standby-L3
RID: 10.20.255.4
Priority: 100 (Standby)
Dual Edge Routers with Backup
Branch-CORE
RID: 10.20.200.1 | HSRP Priority: 110
Primary WAN
Standby-Router
RID: 10.20.200.2 | HSRP Priority: 100
Secondary
Serial Backup: 128 kbps link between routers (10.20.2.0/30)
LACP Port-Channel 1
3x GigabitEthernet links bundled between core switches for load balancing and redundancy
OSPF Area 1 with Summarization
Route summarization configured on Branch-CORE: 10.20.1.0/24 and 10.20.2.0/24 summarized
VLAN Structure (6 VLANs)
VLAN | Department | Network | Gateway
10 | Management | 10.20.10.0/24 | 10.20.10.1
20 | IT Department | 10.20.20.0/24 | 10.20.20.1
30 | Sales | 10.20.30.0/24 | 10.20.30.1
40 | CEO-Admin | 10.20.40.0/24 | 10.20.40.1
50 | Voice | 10.20.50.0/24 | 10.20.50.1
100 | Servers | 10.20.100.0/24 | 10.20.100.1
Server Infrastructure
📡 DHCP Server
IP: 10.20.100.10 | 6 DHCP pools | 245 users per pool
🌐 DNS Server
IP: 10.20.100.11 | Domain: b2pesi.com
📧 EMAIL Server
IP: 10.20.100.12 | Domain: pesi.com
VoIP System
4
IP Phones
2001-2004
Extensions
Inter-Branch Calling: Branch 2 ↔ HQ (6001-6005) via OSPF routing
IP Scheme: 10.20.0.0/16 | OSPF Area: Area 1 | Capacity: ~1,200 users

## Slide 9
BRANCH NETWORKS
Branch 2: Distributed Offices
Contrasting architectures: basic services vs. complex independent connectivity
B2
Branch 2
Network Overview
IP Range: 172.16.0.0/16
Domain: b1pesi.com
VLANs: 6 department VLANs
Server Infrastructure
📡 DHCP Server
IP: 172.16.60.2 | 6 pools | ~1,200 users
🌐 DNS Server
IP: 172.16.60.3 | Domain: b1pesi.com
📧 EMAIL Server
IP: 192.168.60.2 | Domain: b1pesi.com
Characteristics
Simple branch with basic services
6 VLANs serving 5 departments
Centralized server farm
B2
Branch 2
Advanced Features
IP Range: 172.16.0.0/16
OSPF Area: Area 3
WAN: Dual ISP connectivity
NAT: PAT (Port Address Translation)
Core Infrastructure
B2-Core-Router
RID: 4.4.4.4
B2-Core-Router-2
RID: 3.3.3.3 (NAT)
B2-Core-Switch-1
RID: 1.1.1.1 (Active)
B2-Core-Switch2
RID: 2.2.2.20 (Standby)
Unique Capabilities
Only branch with NAT/PAT
Direct dual ISP internet
Full mesh router-switch connectivity
Can function independently from HQ
⚠️ CRITICAL NOTE
B1 & B4 share 172.16.0.0/16
Branch 1
Basic infrastructure
Branch 4
Complex independent

## Slide 10
03
Emergency
Response System
Mission-critical network infrastructure
for emergency services with extreme redundancy
10
VLANs
Emergency services
4
Critical Services
Life-saving teams
570+
Device Capacity
Mission-critical
EXTREME REDUNDANCY
Zero single point of failure for life-critical emergency response operations

## Slide 11
EMERGENCY RESPONSE
Branch 3 (E-Site): Emergency Network
Life-critical infrastructure with load-balanced HSRP and dedicated emergency services
Emergency Services VLANs
🚑 Ambulance
VLAN 10
Network: 10.10.10.0/24 | Gateway: 10.10.10.1
🏥 Medical
VLAN 20
Network: 10.10.20.0/24 | Gateway: 10.10.20.1
👮 Police
VLAN 30
Network: 10.10.30.0/24 | Gateway: 10.10.30.1
🚒 Rescue
VLAN 40
Network: 10.10.40.0/24 | Gateway: 10.10.40.1
Load-Balanced HSRP Configuration
E-Core-1 Active: VLAN 10,20,30,50,70,80,90
E-Core-2 Active: VLAN 40,60 (Rescue & IT)
Additional VLANs
Voice: 10.10.50.0/24 | IT: 10.10.60.0/24 | Wireless: 10.10.70.0/24
IoT: 10.10.80.0/24 | Servers: 10.10.90.0/24 | Management: 10.10.99.0/24
Emergency Server Farm (VLAN 90)
📡 DHCP Server
IP: 10.10.90.11 | 9 pools | 570+ device capacity
🌐 DNS Server
IP: 10.10.90.10 | Domain: emergency.com
📧 EMAIL Server
IP: 10.10.90.13 | Domain: helpline.centre
🔐 AAA/RADIUS Server
IP: 10.10.90.12 | Port: 1645 | Full AAA implementation
📁 FTP Server
IP: 10.10.90.14 | Department-specific user access
🗄️ Database Server
IP: 10.10.90.15 | Emergency records management
Emergency VoIP System
E-Voice-Path (10.10.90.20)
Cisco CME | Max 20 ephones | 10 emergency hotlines
Hotlines
115, 2101, 3001
4001, 5001, 15
1151, 1122, 10001
Inter-Site
→ HQ (6001-6005)
→ Branch 2 (2001-2005)
Emergency calls routed
Network Range: 10.10.0.0/16 | OSPF Area: Area 2 | Domain: emergency.com / helpline.centre

## Slide 12
04
Central
Distribution System
Enterprise hub connecting all sites with
dual firewalls, ISPs, and DMZ services
5
Sites Connected
Full mesh topology
2
ISP Links
PTCL + Nayatel
4
OSPF Areas
Multi-area routing
DUAL SECURITY LAYER
Cisco ASA firewalls with DMZ isolation and IPSec VPN connectivity

## Slide 13
CENTRAL DISTRIBUTION
Central: Hub Architecture & Security
Enterprise distribution with dual firewalls, DMZ, and multi-area OSPF routing
Core Distribution Layer
Central-1 (Primary)
RID: 1.1.1.1 | Area 0 | Connects HQ, Branch 1
Central-2 (ABR)
RID: 2.2.2.2 | Connects Areas 0,1,2,3
Port-channel LACP: 10.255.255.0/30 between Central-1 and Central-2
Dual Firewall Security
FIREWALL-1 (Primary ASA)
Outside1: 203.0.113.6/30 (PTCL) | DMZ: 172.16.1.1/30
FIREWALL-2 (Secondary)
Outside2: 203.0.114.2/30 (Nayatel) | DMZ: 172.16.1.5/30
Security Zones
Inside (100) → DMZ (50) → Outside (0)
DMZ & Public Services
DMZ Switch & Servers
VLAN 10: 172.16.0.0/24 | Gateway: 172.16.0.254
Web: 172.16.0.10
Mail: 172.16.0.11
DNS: 172.16.0.12
FTP: 172.16.0.13
NAT Configuration
VPN Connectivity
IPSec Site-to-Site VPN
Encryption: AES 256-bit | Auth: Pre-shared key
DH Group: Group 5 | Tunnel: EDGE-1 ↔ EDGE-2
Connected Sites: HQ (Area 0) | Branch 2 (Area 1) | Emergency (Area 2) | Branch 4 (Area 3) | Branch 1 (Area 0)

## Slide 14
PESI NETWORK
Complete Network Topology
Enterprise-wide infrastructure interconnecting all sites through central distribution
OSPF Multi-Area Architecture
Site Comparison Overview
Site | IP Range | Area | VLANs
HQ | 50.50.0.0/16 | Area 0 | 9
Branch 2 | 10.20.0.0/16 | Area 1 | 6
Emergency | 10.10.0.0/16 | Area 2 | 10
Branch 4 | 172.16.0.0/16 | Area 3 | 6
Branch 1 | 172.16.0.0/16 | Area 0 | 6
Key Features Comparison
Redundancy
All sites: Dual core switches, dual routers, HSRP/LACP
Security
HQ & Emergency: AAA/RADIUS | Branch 4: NAT/PAT
VoIP
HQ: 5 phones | Branch 2: 4 phones | Emergency: 10 hotlines
Special Features
HQ: IoT Security | Emergency: Load-balanced HSRP | Branch 4: Dual ISP
5
Total Sites
4
OSPF Areas
37
Total VLANs
~5,000
Device Capacity

## Slide 15
ENTERPRISE COMPLETE
PESI: Enterprise-Grade
Infrastructure
Comprehensive network delivering mission-critical emergency services across Pakistan
with zero single points of failure, maximum uptime, and scalable architecture
37
Total VLANs
Department segmentation
100%
Redundancy
No single point of failure
~5,000
Device Capacity
Enterprise scale
24/7
Mission Critical
Always operational
Scalable Design
Hierarchical 3-tier architecture enabling seamless expansion across all emergency services
Maximum Security
Multi-layered security with dual firewalls, AAA/RADIUS, and network segmentation
Future Ready
Advanced VoIP, IoT integration, and converged network services for next-gen emergency response
Prepared by: Abdul Wahid | Project: PESI Network Infrastructure
December 24, 2025